## Slide 1: The IPMC

## Slide 2: Work Shadowing
3 days watching two shifts of the IPMC, 9am – 5pm
Followed Mike McTernan and Paul
Also talked to Graham about SMARTs
Learnt something about the basic structure of 21C network
Learnt something about how the 21C network is monitored, maintained and repaired

## Slide 3: The 21C Network
Access
Metro
Core
MSAN
BRAS
BEA
VLAN to ISP
RADIUS
Harlequin
(e.g Orange, Virgin)
BT Retail
Plusnet
Colossus

## Slide 4: The 21C Network
Core devices are fully meshed.
  (few problems or changes)
Metro and Access devices usually have redundancy.
  Lots of changes made, lots of devices so lots that can go wrong.
Access
Metro
Core

## Slide 5: What the Ops Team Does
Monitors the devices on the 21C network.
Fixes problems picked up through monitoring, or through customer complaints.
‘Customers’ in this case are the ISPs – BT Retail, Orange, Plusnet etc.
Often they simply have to prove traffic loss isn’t caused by a fault on the 21C network.

## Slide 6: Team Structure
Two Alarms Operators
Five Network Engineers
One team supervising 21C, one team supervising 20C
Also RSN and Wifi teams

## Slide 7: Processes
Alarm raised on SMARTs or session drops are recorded by Rabit
Alarms operator verifies fault and attempts any quick fix possible
If problem lasts longer than 10mins they create an incident on IRAMs, and create a ticket on AutoFix
Or a complaint is raised by a customer
Or a request for confirmation is requested by a customer

## Slide 8: Process
IPMC Engineer picks up the Autofix ticket
Uses PACs to find out information about the devices involved
Logs onto the box
Interrogates the box or surrounding boxes
Is this a hardware fault?
What is the single point of failure?
Is there any unusual behaviour?

## Slide 9: Tools
PACS
Autofix
ALS
SMARTS
ESID
SAM

## Slide 10: SMARTS
Often the first sign something is wrong
Must be verified before being acted upon
Polls devices every four minutes
  (so lots of data kept about the system)
  Traffic
  Temperature
  CPU usuage
  Memory
  Fans
  PSUs
Uses PACS to find devices

## Slide 11: SMARTS
Also monitors groups of devices that make up a route or service
Does root-cause analysis when these services go down
Auto-tickets faults straight into AutoFix without bothering the alarms operators
  Does this 90% of the time for Access MSANs

## Slide 12: RABIT
Notifies the Alarms Operators of large amounts of session drops.
Sporadic drops might just be people turning off a router.
Large outages indicate a fault on the network

## Slide 13: PACS
Inventory system
Acts as a map of the network
Physical layer – no VLANs
Really useful, when it is accurate
IPMC only have read access
IPMC has no way of notifying PACs that they have had to modify the network
  This leads to problems as PACs will provision devices that are already in use
  IPMC team work in shifts, meaning it takes longer for the Design Team to catch up
Slow to change

## Slide 14: NH21
Just not used
Clunky
Slow
A better system? One that shows changes on the network:
  e.g differences between now and the same time last week

## Slide 15: ALS
Used to keep a journal of all operations carried out on the network
Allows multiple people to work on the same ticket at different times
Links together all the other numbers and IDs the team has to remember
Records observations and overall progress

## Slide 16: Example Problem
Traffic loss reported by BT Retail.
Problem turns out to be a link has been ‘costed’ wrong.
Links between different devices can be artificially ‘costed’ to make them prefer a route over another
If someone fat-fingers the numbers, a link can end up becoming over-desirable and the over-loaded router at the end of it starts dropping packets
This is particularly tricky as the router may end up being unreachable even to management traffic

## Slide 17: Example Solution
An engineer is sent out to manually log into the router and reconfigure it
This is quite labour-intensive to solve, as the IPMC engineer has to be on the phone to the engineer the entire time to tell him what commands are needed

## Slide 18: Conclusions
SMARTS is not trusted (regarded as about 70% inaccurate)
NH21 is not used
PACs is generally useful as a map
Communication and logging tools are useful (ALS, Autofix, IRAMs)
Utility and speed are key
The IPMC team are perfectly happy to have you follow them around for a while

## Slide 19: Conclusions
Data analysis?
  The IPMC only really examine the network in the short-term
  Smarts
    Needs to be more accurate
    Needs a way to report inaccuracies
    Could predict or catch more subtle network problems
    Examine behaviour over long period of time